## Slide 1: Acoustic Signatures of Quadcopter Propellers

## Slide 2: Context and application
Public perception of drones is poor due to the annoying sound that they make.
This, and other legislative barriers, prevent the adoption of drone-based services in urban environments.
Recent research has focused on optimising aerodynamic and aeroacoustics performance to overcome these barriers.

## Slide 3: Objectives
Design and build an experimental setup to measure aerodynamic performance and acoustic signatures of various propeller designs
Attribute changes in the acoustic spectrum to flow phenomena caused by propeller geometry modifications.
Analyse psychoacoustic performance

## Slide 4: Propeller geometry
Consideration for Toroidal designs
Previous research has covered:
  Tip geometry
  Blade sweep
  Blade spacing
  Trailing edge serrations
Varying blade span
TOROIDAL PROPELLERS

## Slide 5: Hypothesis
Improvements in efficiency

## Slide 6: Aerodynamic performance
Aerodynamic performance quantities
Power is obtained from
Require values for torque, thrust and angular speed.
Notes: For the experimental setup it's important to consider the parameters needed to define a given propellers performance. Dimensionless thrust and power coefficients can be found from blade tip speed and area. The ratio of these coefficients define a ‘static’ efficiency which is different to the typical propulsive efficiency. The values then required to be measured are the torque, thrust and angular speed.
Dynamic measurements of torque and angular velocity could be fused together in a Kalman filter

## Slide 7: Aerodynamic measurements
Torque and thrust measured by strain gauge load cells
Full bridge cantilever models selected for sensitivity and resistance to off-axis forces
Orientation selected for accuracy, and ease of calibration
CAD
Notes: To measure torque and thrust the deflection of load cells will be measured by strain gauges. This was preferred over null force balancing methods for its simple setup and ability to measure dynamic torque.

## Slide 8: Acoustic performance
To quantify the annoyance of sound the psychoacoustics must be considered
Psychoacoustic metrics of loudness, fluctuation strength, roughness, sharpness, tonality

## Slide 9: Questions?
Toroidal propeller designs – Thingyverse
Owl image – Wang and Liu
References